Tender Specification HK Audio TB-R T-Bracket

Mechanical mounting and alignment system for professional sound reinforcement loudspeakers.

The universal tilt rail shall be made of high strength steel and shall be galvanized and powder coated for surface protection. The tilt rail shall allow universal mounting to truss spars, ceilings, wall outlets and beams. Speaker angle adjustments in the range of +5° to -45° shall be possible along the graduated perforated rail. The tilt rail shall be suitable for supporting heavy loudspeakers (WLL = 70 kg).

The mechanical mounting and alignment system shall be HK Audio TB-R T-Bracket.