Tender Specification HK Audio VORTIS (2) Wall Plate

Professional wall mounting plate for mounting speaker systems on walls and/or the ceiling.

The wall mounting plate shall provide the ability to rotate the mounted speaker systems in increments of 5°.

The mechanical connection shall be of a self-locking design and shall be made either directly with the U-bracket attached to the loudspeaker or via an additional tilting device mounted in between.

The wall mounting plate shall be capable of supporting a fanned out multiple array of at least two professional sound reinforcement loudspeakers (WLL 70 kg).

The wall mounting plate shall be the HK Audio VORTIS (2) Wall Plate.